Grating Testing Apparatus (GTA)

User's Manual

Casey Deen

8 February 2011

Transmission Testing

1. Start the Labview motor control VI (GT_server_v2.vi). This VI waits for approximately 1 minute to establish a IP connection to the python program. After the connection is established, it will wait indefinitely for commands from the python program over the IP connection.
2. Open the transmission.py python script in the python IDLE. Press F5 to start.
  1. The script will load in the defaults from the grating_test.config.txt file.
  2. The motor controller, if configured correctly, will send the motor searching for its home position. Be sure to start the program with the detector arm clock-wise from its home location. If you fear the detector arm